## Slide 1
Introduction to Layering &
Network Layering
COS 316: Principles of Computer System Design
Lecture 7
Wyatt Lloyd & Rob Fish

## Slide 2
“Modularity based on abstraction is the way things get done”
2009 Turing Award Lecture
Barbara Liskov
Notes: Venus Operating System (1970): Virtual Machines
CLU programming language – modular programming, data abstraction (data types, function, abstract classes with inheritance)
Viewstamped Replication – Collection of machines that fail as single non-failing machine -> datacenter systems – 418!
Practical Byzantine Fault Tolerance – Collection of machines that fail and some are evil as single non-failing machine -> blockchain

## Slide 3: Modularity Through Layering
Systems on systems on systems though layering
Each layer hides complexity with abstraction
Network layers today!

## Slide 4: The Problem of Communication
Re-implement every application for every new underlying transmission medium?
Change every application on any change to an underlying transmission medium?
No! But how does the Internet design avoid this?
Applications
Transmission
media
Facetime
HTTP
SSH
FTP
Coaxial cable
Fiber optic
Wi-Fi

## Slide 5: Solution: Layering
Intermediate layers provide a set of abstractions for applications and media
New applications or media need only implement for intermediate layer’s interface
Applications
Transmission
media
Facetime
HTTP
SSH
FTP
Coaxial cable
Fiber optic
Wi-Fi
Intermediate layers

## Slide 6: The Art of Layering
How many layers?
What goes in each layer?
What abstraction (interface) does each layer provide?
Notes: Discuss, why not too many layers? Often some loss of efficiency with each layer, either implementation or fundamental.

## Slide 7: Layering in the Internet
Transport: Provide end-to-end communication between processes on different hosts
Network: Deliver packets to destinations on other (heterogeneous) networks
Link: Enables end hosts to exchange atomic messages with each other
Physical: Moves bits between two hosts connected by a physical link
Applications
Transport layer
Network layer
Link layer
Physical layer
Host

## Slide 8: Logical Communication Between Layers
How to forge agreement on the meaning of the bits exchanged between two hosts?
Protocol: Rules that govern the format, contents, and meaning of messages
  Each layer on a host interacts with its peer host’s corresponding layer via the protocol interface
Application
Transport
Network
Link
Physical
Network
Link
Physical
Application
Transport
Network
Link
Physical
Host A
Host B
Router

## Slide 9: Physical communication
Communication goes down to the physical network
Then from network peer to peer
Then up to the relevant application
Application
Transport
Network
Link
Physical
Network
Link
Physical
Application
Transport
Network
Link
Physical
Host A
Host B
Router

## Slide 10: Communication Between Peers
How do peer protocols coordinate with each other?
Layer attaches its own header (H) to communicate with peer
  Higher layers’ headers, data encapsulated inside message
    Lower layers don’t generally inspect higher layers’ headers
Application
Transport
Network
Application message
H
H
Transport-layer message body
Network-layer datagram body

## Slide 11: Internet Protocol Layers
Local packet delivery
Global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application
HTTP …
IP
Ethernet, Optical, WiFi, …
TCP, UDP
Notes: Physical layer underneath this too

## Slide 12: IP is the “Narrow Waist” of the Internet
The network layer protocol
  Enables portability above and below
Lots of link layer protocols underneath
Several transport protocols on top
  TCP, UDP, QUIC

## Slide 13: IP: Best-Effort Global Packet Delivery
Data
Never having to say you’re sorry
  Don’t have to reserve bandwidth and memory
  Don’t have to do error detection and correction
  Don’t have to remember anything from one packet to the next
Easier to survive failures
  Transient disruptions are okay during failure recovery
Can run on nearly any link technology
  Greater interoperability and evolution
  RFC 1149…
Notes: RFC 1149: A Standard for the Transmission of IP Datagrams on Avian Carriers (released April 1, 1990)

## Slide 14: Transport: Application to Application
Network layer is host-to-host
Transport layer is port-on-host-to-port-on-host
  think application to application
  demultiplexing
  e.g., port 80 is HTTP, port 443 is HTTPS, port 22 is SSH
Why transport and not network layer?
Notes: two big reasons: 1) keep network layer simple
2) ports are end-host identifiers ... irrelevant to routers in between the end hosts!

## Slide 15: Transport: Application to Application
Network doesn’t have error detection
Transport layer does have error detection
Why transport and not network layer?
Why not both?
Notes: Errors are rare... (tell them this)
Transport layer: only do once for each global packet delivery
Network layer: would have to do many times for each global packet delivery
Also transport is closer to application, can do fancier error correction

## Slide 16: Transport: Transmission Control Protocol (TCP)
Ordered, reliable stream of bytes
  Built on top of best-effort packet delivery at the network layer
Challenges with IP
  Lost or delayed packets
  Corrupted packets
  Out-of-order packet arrivals
  Receiver runs out of space
  Network cannot handle current load

## Slide 17: TCP: Lost or Delayed Packets
Problem: Lost or delayed data
Solution: Timeout and retransmit
  Receiver sends acknowledgement of data

## Slide 18: TCP: Corrupted Data
Problem: Data corrupted during transmission
Solution: checksums
Sender computes a checksum 134
  Sender sums up all bytes in the payload + 212
  And sends the sum to the receiver = 346
Receiver checks a checksum 134
  Recevier sums up all bytes in the payload + 216
  And compares against the checksum = 350
Then what?
Notes: Draw on board: get index.html -- get indeY.html

## Slide 19: TCP: Out-of-Order Packet Arrivals
Problem: Our of order packets:
  Application: GET index.html
  Sent packets: |GET| |inde| |x.ht| |ml|
  Received packets: |ml| |inde| |x.ht| |GET|
Solution: Add sequence numbers
  Received packets: |4|ml| |2|inde| |3|x.ht| |1|GET|

## Slide 20: TCP: Receiver Runs Out of Space
Problem: No more space to receive packets
Solution: Flow control
  Receiver maintains a window size
    Amount of data it can buffer
  Advertises window to the sender
    Amount sender can send without acknowledgement
  Ensures that sender does not send too much

## Slide 21: TCP: Network that Cannot Handle the Load
Problem: Too many packets at once
Solution: Congestion control
  Future lectures!

## Slide 22: TCP’s reliable byte stream
Notes: Draw on board: App sends IP packets: [_____] [______] [__X____] [_________
2nd packet is lost (erase)
3rd packet is corrupted
4th packet is received
2nd packet resent
3rd packet resent
Deliver in order 3->2
Draw them showing up and filling into the contiguous byte stream on the receiver!
App 1 on left
Network in between
App 2 on right

## Slide 23: Transport: User Datagram Protocol (UDP)
Datagram of bytes
  A message
Challenges with IP
  Lost or delayed packets X
  Corrupted packets √
  Out-of-order packet arrivals X
  Receiver runs out of space X
  Network cannot handle current load X
UDP does less than TCP, why do we want UDP too?
Notes: Transport layer: do

## Slide 24: Layering & Network Layers Conclusion
The art of layering
Network layers
  Protocol, headers, encapsulation
IP layer: best-effort global packet delivery between host
TCP layer: ordered, reliable byte stream between applications