## Slide 1: Logic: From Greeks to philosophers to circuits.
COS 116, Spring 2012
Adam Finkelstein

## Slide 2: High-level view of self-reproducing program
Print 0
Print 1
. Print 0
. . . . . .
. . . . . .
. . . . . .
}
Prints binary code of B
}
Takes binary string on tape, and …
A
B
SEE HANDOUT ON COURSE WEB

## Slide 3: Binary arithmetic
    25
    + 29
    54
    11001
    11101
    110110
Q: How do we add two binary numbers?

## Slide 4: Recap: Boolean Logic Example
Ed goes to the party if Dan does not and Stella does.
Choose “Boolean variables” for 3 events:
E: Ed goes to party
D: Dan goes to party
S: Stella goes to party
}
{
Each is either TRUE or FALSE
E = S AND (NOT D)
Alternately: E = S AND D

## Slide 5: Three Equivalent Representations
Boolean Expression E = S AND D
Truth table: Value of E for every possible D, S. TRUE=1; FALSE= 0.
0
0
1
0
1
1
1
1
0
0
0
0
E
S
D
Boolean Circuit
E
S
D

## Slide 6: Boolean “algebra”
A AND B written as A  B A OR B written as A + B
0 + 0 = 0
1 + 0 = 1
1 + 1 = 1
0  0 = 0
0  1 = 0
1  1 = 1
Funny arithmetic
Notes: This is just notation.

## Slide 7: Claude Shannon (1916-2001) Founder of many fields (circuits, information theory, artificial intelligence…)
With “Theseus” mouse

## Slide 8: Boolean gates
Output voltage is high if both of the input voltages are high; otherwise output voltage low.
High voltage = 1
Low voltage = 0
Shannon (1939)
x
y
x · y
x
y
x + y
Output voltage is high if either of the input voltages are high; otherwise output voltage low.
x
x
Output voltage is high if the input voltage is low; otherwise output voltage high.
(implicit extra wires for power)

## Slide 9: Let’s try it out…
Boolean Expression E = S AND D
Truth table: Value of E for every possible D, S. TRUE=1; FALSE= 0.
0
0
1
0
1
1
1
1
0
0
0
0
E
S
D
Boolean Circuit
E
S
D

## Slide 10: Combinational circuit
Boolean gates connected by wires
Important: no cycles allowed
Wires: transmit voltage
(and hence value)

## Slide 11: Examples
(Sometimes we use this
for shorthand)
4-way AND
More complicated example
 Crossed wires that are not connected are sometimes drawn like this.
(or this)
Notes: Work out truth table for bottom circuit

## Slide 12: Combinational circuits and control
“If data has arrived and packet has not been sent, send a signal”
Data arrived?
Packet sent?
S
D
P
Send signal
S = D AND (NOT P)

## Slide 13: Circuits compute functions
Every combinational circuit computes a Boolean function of its inputs
Inputs
Outputs

## Slide 14: Ben Revisited
B: Ben Bikes
R: It is raining
E: There is an exam today
O: Ben overslept
Ben only rides to class if he overslept, but even then if it is raining he’ll walk and show up late (he hates to bike in the rain). But if there’s an exam that day he’ll bike if he overslept, even in the rain.
How to write a boolean expression for B in terms of R, E, O?
Notes: Work out truth table

## Slide 15: Ben’s truth table
O | R | E | B
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 16: Truth table  Boolean expression
Use OR of all input combinations that lead to TRUE (1)
B = O·R·E + O·R·E + O·R·E
O | R | E | B
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Note: AND, OR, and NOT gates suffice to implement every Boolean function!

## Slide 17: Sizes of representations
For k variables:
A | B | … | X
0 | 0 | … | 0
0 | 0 | … | 0
0 | 1 | … | 0
0 | 1 | … | 1
… | … | … | …
… | … | … | …
1 | 1 | … | 1
k + 1
2k
k | 10 | 20 | 30
2k | 1024 | 1048576 | 1073741824
For an arbitrary function, expect roughly half of X’s to be 1 (for 30 inputs roughly 1/2 billion!) Tools for reducing size: (a) circuit optimization (b) modular design

## Slide 18: Expression simplification
Some simple rules:
  x + x = 1
  x · 1 = x
  x · 0 = 0
  x + 0 = x
  x + 1 = 1
  x + x = x · x = x
  x · (y + z) = x · y + x · z
  x + (y · z) = (x+y) · (x+z)
x · y + x · y
= x · (y + y)
= x · 1
= x
De Morgan’s Laws:
x · y = x + y
x + y = x · y

## Slide 19: Simplifying Ben’s circuit
…
Notes: Draw this

## Slide 20: Something to think about: How hard is Circuit Verification?
Given a circuit, decide if it is “trivial” (no matter the input, it either always outputs 1 or always outputs 0)
Alternative statement: Decide if there is any setting of the inputs that makes the circuit evaluate to 1. Time required?

## Slide 21: Boole’s reworking of Clarke’s “proof” of existence of God (see handout – after midterm)
General idea: Try to prove that Boolean expressions E1, E2, …, Ek cannot simultaneously be true
Method: Show E1· E2 · … · Ek = 0
Discussion for after Break: What exactly does Clarke’s “proof” prove? How convincing is such a proof to you?
Also: Do Google search for “Proof of God’s Existence.”

## Slide 22: Beyond combinational circuits …
Need 2-way communication (must allow cycles!)
Need memory (scratchpad)
CPU
Ethernet card

## Slide 23: Circuit for binary addition?
Want to design a circuit to add any two N-bit integers.
Q: Is the truth table method useful for N=64?
    25
    + 29
    54
    11001
    11101
    110110

## Slide 24: After Break: Modular Design
Design an N-bit adder using N 1-bit adders
After midterm, read: (a) handout on boolean logic.
(b) Boole’s “proof” of existence of God.