## Slide 1: Software-Defined Networks
Jennifer Rexford
Princeton University

## Slide 2: Traditional Networks
control plane: distributed algorithms
data plane: packet processing

## Slide 3: Software Defined Networks
decouple control and data planes

## Slide 4: Software Defined Networks
decouple control and data planes by providing open standard API

## Slide 5: Simple Data-Plane API
Prioritized list of rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
srcip=1.2.*.*, dstip=3.4.5.*  drop
srcip=*.*.*.*, dstip=3.4.*.*  forward(2)
3. srcip=10.1.2.3, dstip=*.*.*.*  send to controller

## Slide 6: (Logically) Centralized Controller
Controller Platform

## Slide 7: Protocols  Applications
Controller Platform
Controller Application

## Slide 8: Seamless Mobility
See host sending traffic at new location
Modify rules to reroute the traffic

## Slide 9: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*,
dst=1.2.3.4
src=1*,
dst=1.2.3.4
10.0.0.1
10.0.0.2

## Slide 10: Middlebox Traffic Steering
Direct selected traffic (e.g., port 80)
… through a chain of middleboxes
dstip = 1.2.3.4
dstport = 80
dstip=1.2.3.4

## Slide 11: Example SDN Applications
Seamless mobility and migration
Server load balancing
Steering traffic through middleboxes
Dynamic access control
Using multiple wireless access points
Energy-efficient networking
Blocking denial-of-service attacks
Adaptive traffic monitoring
Network virtualization
<Your app here!>

## Slide 12: A Major Trend in Networking
SDN components
  Switches: Open vSwitch, hardware switches, etc.
  Controllers: ONOS, Floodlight, Ryu, Frenetic, …
Commercial successes
  Google’s private backbone
  Nicira’s network virtualization platform
Industry consortia
  Open Networking Foundation (ONF)
  Open DayLight (ODL)
  Open Compute Project (OCP)

## Slide 13: Example Research Areas

## Slide 14: Languages and Verification
Languages
  Abstractions for apps
  Compilation to switches
Verification
  Data-plane invariants
  Control-plane correctness
Controller
App
App
queries
updates
composition
Controller

## Slide 15: Distributed Controllers
Controller
Controller
Scalability, reliability, and performance
Managing controller state or replicas
Aggregating information about the network

## Slide 16: More Sophisticated Switches
OpenFlow 1.0
  Single rule table and twelve header fields
OpenFlow 1.3/1.4
  Multiple match-action stages on different headers
OpenFlow 2.0 (?)
  Reconfigurable parsing and match-action tables
White-box/bare-metal switches
  Program the switch directly

## Slide 17: Network Function Virtualization
Network functions
  Firewall, intrusion detection, NAT, transcoder, compression, proxy cache, monitoring, …
Virtualized
  Virtual machines that can run anywhere
Challenges
  Optimization (placement, steering, routing)
  Platforms for hosting virtualized functions
  Control protocols for managing the functions

## Slide 18: SDN Security
Securing the entire stack
  Switches
  Control protocol
  Controller platform
  Controller apps
Example attacks/vulnerabilities
  Worst-case traffic to DoS the controller
  Rogue apps that violate user privacy
  Compromising the controller platform
Controller
App
App

## Slide 19: New Applications of SDN
Cloud
  Data centers
  Private backbones
Other networks
  Enterprise
  Cellular
  Home
  Exchange points
  Optical networks
Hybrid deployments
  Overlay (SDN edge, legacy core)
  Mix of SDN and legacy devices
Beyond networking
  Software Defined Infrastructure
  Network, middleboxes, storage, compute, …

## Slide 20: Conclusions
SDN is two main ideas
  Logically centralized controller
  Standard APIs to the data plane
SDN is happening in practice
  Protocol standards and white-box networking
  Wide variety of switch and controller platforms
  Real operational deployments
Clean-slate research opportunity
  … while still influencing the practice