## Slide 1: SDN Applications
Jennifer Rexford
Princeton University
Notes: Goals: use example applications to illustrate challenges in PL and verification, and hopefully also highlight some new apps that are neat

## Slide 2: Software-Defined Networking
Controller
App 1
App 2
Logically-centralized controller
Simple data-plane interface

## Slide 3
Prioritized list of rules
  Priority: disambiguate overlapping patterns
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Counters: number of bytes and packets
Priority | Pattern | Actions | Counters
3 | srcip=1.0.*.* | Forward(1) | 3, 4500
2 | dstip=1.2.3.4, dstport=80 | dstip:=10.0.0.1, Forward(2) | 5, 6018
1 | srcport=25 | Send to controller | 1, 512
0 | * | Drop | 2, 1024

## Slide 4: Example SDN Applications
MAC learning
Stateful firewall
Server load balancing
Wide-area traffic engineering
Middlebox traffic steering
Internet eXchange Points
Traffic monitoring

## Slide 5: Programming & Verification Challenges
Multiple tasks, one set of rules
Policies that change over time
Uncertain ordering of events
Rule-space limitations
Non-deterministic applications
Interactions with other protocols

## Slide 6: MAC Learning
Plug-and-play
  Flood packets sent to unknown destinations
  Learn a host’s location when it sends packets
Example
  h1 sends to h2: flood, learn (h1, port 1)
  h3 sends to h1: forward to port 1, learn (h3, port 3)
  h1 sends to h3: forward to port 3
h1
h2
h3
1
2
3

## Slide 7: MAC Learning, Done Wrong
Install rules as you learn
  Match on host address and port
Buggy behavior
  What happens when h3 sends to h1?
  What happens when h1 sends to h3?
Pattern | Action
* | Send to controller
Pattern | Action
dstmac=h1 | Forward(1)
* | Send to controller
h1 sends to h2
h1
h2
h3
1
2
3

## Slide 8: MAC Learning, Stating Invariant
What is the invariant being violated?
  “Reachability between all pairs of hosts”?
  No, h1 can reach h3, albeit via flooding
Performance invariants are hard to state
  “After h3 sends a packet, all other hosts should be able to reach h3 without flooding”?
  Delays between h3 and the switch(es)?
  “After packet from h3 is delivered, all other hosts should reach h3 without flooding”?

## Slide 9: MAC Learning, Done Right
Compose forwarding and querying
  Forwarding: flood or forward
  Query: learn location of unknown hosts
Synthesize a single set of rules
Well, still ignoring that hosts can move…
  Must learn the host’s new location (how?)
Pattern | Action
srcmac=h3, dstmac=h1 | Forward(1)
* | Send to controller
Notes: Should I look at fast mobility, where it isn’t clear which switch has the host?

## Slide 10: Stateful Firewall
Speak only when spoken to
  Client sends a packet to a server
  Only then can a server send a return packet
Example
  s3 sends to c1: block (or blacklist s3)
  c2 sends to s4: forward to port 3
  s4 sends to c2: forward to port 2
Stating the invariant?
c1
c2
s3
1
2
3
s4

## Slide 11: Stateful Firewall, Done Wrong
Bad performance optimization
  Send client packet to server
  And, send copy of packet to controller
But, timing delays
  What if s4 sends back to c2 before the controller installs the rules?
Pattern | Action
srcip=client | Forward(3), send to controller
srcip=server | Drop
c2 sends to s4
Pattern | Action
srcip=c2, dstip=s4 | Forward(3)
srcip=s4, dstip=c2 | Forward(2)
srcip=client | Forward(3), send to controller
srcip=server | Drop

## Slide 12: Stateful Firewall, Done Wrong
Blacklisting instead of blocking
  Unsolicited traffic leads to blacklisting of host
Pattern | Action
srcip=client | Forward(3), send to controller
srcip=server | Send to controller
Two events
  c2’s packet reaches controller: allow s4
  s4’s packet reaches controller: blacklist s4
Which event happens first???
c1
c2
s3
1
2
3
s4
Notes: Similar problem with host mobility – may not be clear which mobility event happened first

## Slide 13: Stateful Firewall, Done Right
No assumptions about delays
  Ordering of events in the switch
  Ordering of events triggered by hosts
Don’t let host see packet
  Until policy is updated
Pattern | Action
srcip=client | Send to controller
srcip=server | Drop
c2 sends to s4
Pattern | Action
srcip=c2, dstip=s4 | Forward(3)
srcip=s4, dstip=c2 | Forward(2)
srcip=client | Send to controller
srcip=server | Drop

## Slide 14: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
srcip=0*,
dstip=1.2.3.4
srcip=1*,
dstip=1.2.3.4
10.0.0.1
10.0.0.2

## Slide 15: Server Load Balancing
Bring up a third server to handle the load
E.g., srcip=10* vs. srcip=11*
srcip=0*,
dstip=1.2.3.4
srcip=1*,
dstip=1.2.3.4
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 16: Load Balancing, Connection Affinity
Connection Affinity
  Connections finish where they started
Ongoing connections
  srcip=1*: finish with server 10.0.0.2
New connections
  srcip=10*: go to 10.0.0.2
  srcip=11*: go to 10.0.0.3
10.0.0.2
10.0.0.3
srcip=1*,
dstip=1.2.3.4
srcip=11*
srcip=10*
3
2
1

## Slide 17: Connection Affinity, Done Wrong
Identifying ongoing connections
  Send a packet to the controller
  See if the packet is a TCP SYN
Timeout the “send to controller rule”
Pattern | Action
srcip=11* | Send to controller
SYN packet from srcip=111
Pattern | Action
srcip=111 | Forward(3)
srcip=11* | Send to controller
Pattern | Action
srcip=110 | Forward(2)
srcip=111 | Forward(3)
srcip=11* | Send to controller
non-SYN packet from srcip=110

## Slide 18: Connection Affinity, Done Wrong
Flawed assumption about TCP protocol
  Just one SYN packet per connection
Duplicate SYN packets
  Network can sometimes duplicate packets
  Sender may retransmit the SYN packet
Misclassification of a connection
  Ongoing connection misclassified as new
How to state the invariant here?

## Slide 19: Server Load Balancing
Weighted traffic splitting
  E.g., {1/6, 1/3, 1/2} to three servers
Matching on header fields
  srcip=000*: 1/8
  srcip=0*: 3/8
  srcip=1*: 1/2
Could do better with more rules
  Better programming abstractions
  Optimizing use of rule-table space

## Slide 20: Wide-Area Traffic Engineering
Compute k paths between edge pairs
Split traffic over the k paths
Adapt to changes in offered load

## Slide 21: Wide-Area TE, What-If Analysis
Planned maintenance
  Before taking link/switch down for maintenance
  … model what the effects will be
SDN to the rescue
  Simply run the controller application
  … using estimated traffic demands
  … and the link or switch removed
Do you necessarily get the same answer
  As you would get in the operational network?
  Hint: what if the order of events matters!

## Slide 22: Wide-Area TE, Transient Behavior
Adapt traffic splitting at multiple switches
Consistent update to preserve invariants
  Congestion-free, loop-free, etc.
A
B
C
Path 1
Path 1
Path 2
Path 2

## Slide 23: Middlebox Traffic Steering
Direct selected traffic (e.g., TCP port 80)
… through a chain of middleboxes
dstip = 1.2.3.4
dstport = 80
dstip=1.2.3.4

## Slide 24: Middlebox Traffic Steering
Unified policy framework
  Switch rules and network paths
  Chains of middleboxes
Joint optimization
  Sizing: how many middlebox instances
  Placement: where to run them
  Steering: which flows to direct through them
  Routing: which network paths to take
Correctness under dynamics

## Slide 25: Software-Defined eXchanges (SDX)
AS A Router
AS C Router
AS B Router
BGP Session
SDN Switch
SDX Controller
SDX

## Slide 26: SDX Apps: Inbound TE
AS C splits incoming traffic
  Web traffic via C1
  Remaining traffic via C2
AS A Router
AS C Routers
AS B Router
C1
C2
Incoming Data

## Slide 27: SDX Apps: DoS Mitigation
Victim AS drops traffic
  Installing drop rules in SDX
AS 2
AS 1
AS 3
SDX 1
SDX 2
Attacker
Victim

## Slide 28: SDX Challenges: Multiple ASes
Combine multiple policies
Virtual switch abstraction
AS A
C1
C2
B1
A1
AS C
AS B
match(dstport=80)drop
match(dstport=80)fwd(C1)
Virtual Switch
Virtual Switch
Virtual Switch
Switching Fabric

## Slide 29: SDX Challenges: Work with BGP
Interdomain routing
  ASes decide who can route through them
  Prevent loops and protocol oscillation
A
C
B
SDX
10.0.0.0/8
20.0.0.0/8
p
match(dstport=80) -> forward(C)

## Slide 30: Traffic Monitoring
Traffic matrix
  Offered load for ingress-egress pairs
Congested link diagnosis
  Fan in/out of a congested link
Denial of service attack diagnosis
  Sink tree into the victim
Localizing packet loss
  Identifying which hop on a path drops packets
Firewall evasion
  Identifying packets that do not traverse a firewall

## Slide 31: Traffic Monitoring Challenges
Generality
  Programming abstractions that support a wide range of queries
Efficiency
  Limiting overhead for collecting and joining data
Accuracy
  Direct observation of the traffic
Dynamics
  Robustness to changing forwarding policy
Limited switch functionality
  Match packets, and count or send to controller

## Slide 32: Traffic Monitoring, Abstractions
Path queries
  Regular expression over predicates on packet location and header values
  SQL groupby constructs to aggregate results
Examples
  Traffic matrix: ingroup(ingress(), [switch]) ^ true* ^ outgroup(egress(), [switch])
  Firewall evasion: in(ingress()) ^ (in(sw!=FW))* ^ out(egress)

## Slide 33: Traffic Monitoring, Compilation
Convert regular expression into a DFA
  DFA tracks packet’s progress in satisfying query
Represent the DFA in the switches
  State: tag on the packet
  Transitions: match-action rules in the switch
  Accepting: count or send packet to controller
0
1
2
sw=S1
sw=S4
Simple query
in(sw=S1) ^ in(sw=S2)

## Slide 34: Conclusions
SDN enables many new apps
These apps raise new challenges
  Programming abstractions
  Verification problems
Lots more work to do!