## Slide 1: HULA: Scalable Load Balancing Using Programmable Data Planes
Naga Katta1
Mukesh Hira2, Changhoon Kim3, Anirudh Sivaraman4,
Jennifer Rexford1
1.Princeton 2.VMware 3.Barefoot Networks 4.MIT

## Slide 2: Datacenter Load Balancing
Multiple network paths
High bisection bandwidth
Volatile traffic
Multiple tenants

## Slide 3: A Good Load Balancer
Multiple network paths
  Track path performance
  Choose best path
High bisection bandwidth
Volatile traffic
Multiple tenants

## Slide 4: A Good Load Balancer
Multiple network paths
  Track path performance
  Choose best path
High bisection bandwidth
  Fine grained load balancing
Volatile traffic
Multiple tenants

## Slide 5: A Good Load Balancer
Multiple network paths
  Track path performance
  Choose best path
High bisection bandwidth
  Fine grained load balancing
Volatile traffic
  In-dataplane
Multiple tenants

## Slide 6: A Good Load Balancer
Multiple network paths
  Track path performance
  Choose best path
High bisection bandwidth
  Fine grained load balancing
Volatile traffic
  In-dataplane
Multiple tenants
  In-network

## Slide 7: CONGA (SIGCOMM’14)

## Slide 8: Datapath LB: Challenges
Tracks all paths

## Slide 9: Datapath LB: Challenges
Tracks all paths
Large FIBs

## Slide 10: Datapath LB: Challenges
Tracks all paths
Large FIBs
Custom ASIC

## Slide 11: Programmable Commodity Switches
Vendor agnostic
  Uniform programming interface (P4)
  Today’s trend -> cheaper
Reconfigurable in the field
  Adapt or add dataplane functionality
Examples
  RMT, Intel Flexpipe, Cavium Xpliant, etc.

## Slide 12: Programmable Switches - Capabilities
Memory
M | A
m1 | a1
Ingress Parser
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Egress Deparser
Queue Buffer
P4 Program
Compile
More than OF 1.X

## Slide 13: Programmable Switches - Capabilities
Memory
M | A
m1 | a1
Ingress Parser
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Egress Deparser
Queue Buffer
P4 Program
Compile
More than OF 1.X
Programmable Parsing

## Slide 14: Programmable Switches - Capabilities
Memory
M | A
m1 | a1
Ingress Parser
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Egress Deparser
Queue Buffer
P4 Program
Compile
More than OF 1.X
Programmable Parsing
Match-Action
Pipeline

## Slide 15: Programmable Switches - Capabilities
Memory
M | A
m1 | a1
Ingress Parser
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Egress Deparser
Queue Buffer
P4 Program
Compile
More than OF 1.X
Programmable Parsing
Match-Action
Pipeline
Register Array

## Slide 16: Programmable Switches - Capabilities
Memory
M | A
m1 | a1
Ingress Parser
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Egress Deparser
Queue Buffer
P4 Program
Compile
More than OF 1.X
Programmable Parsing
Match-Action
Pipeline
Stateful
Memory
Switch
Metadata

## Slide 17: Hop-by-hop Utilization-aware Load-balancing Architecture
Distance-vector like propagation
  Periodic probes carry path utilization
Each switch chooses best downstream path
  Maintains only best next hop
  Scales to large topologies
Programmable at line rate
  Written in P4.

## Slide 18: HULA: Scalable and Programmable
Objective | P4 feature
Probe propagation | Programmable parsing
Monitor path performance | Link state metadata
Choose best path, route flowlets | Stateful memory and comparison operators

## Slide 19: Probes carry path utilization
ToR
Aggregate
Spines
Probe originates
Probe replicates
Notes: Let’s dig a little deeper. In HULA, the probes originate at the ToRs (through the servers or the ToRs themselves) and then are replicated on multiple paths as they travel the network. We make sure that each switch replicates only the necessary set of probes to the others so that the probe overhead is minimal.

## Slide 20: Probes carry path utilization
ToR
Aggregate
Spines
Probe originates
Probe replicates
P4 primitives
New header format
Programmable Parsing
RW packet metadata
Notes: Let’s dig a little deeper. In HULA, the probes originate at the ToRs (through the servers or the ToRs themselves) and then are replicated on multiple paths as they travel the network. We make sure that each switch replicates only the necessary set of probes to the others so that the probe overhead is minimal.

## Slide 21: Probes carry path utilization
S1
S2
S3
S4
ToR 10
ToR ID = 10 Max_util = 50%
ToR 1
Probe
ToR ID = 10 Max_util = 80%
ToR ID = 10 Max_util = 60%

## Slide 22: Each switch identifies best downstream path
S1
S2
S3
S4
ToR 10
Dst | Best hop | Path util
ToR 10 | S4 | 50%
ToR 1 | S2 | 10%
… | … | 
ToR 1
Best hop table
Probe
ToR ID = 10 Max_util = 50%
Notes: Then the switch takes the minimum from among the probe given utilization and stores it in the local routing table. The switch S1 then sends its view of the best path to the upstream switches. And the upstream switches process these probes and update their neighbours. This leads to a distance vector-style propagation of information about network utilization to all the switches. But at the same time, each switch only needs to keep track of the best next hop towards a destination.

## Slide 23: Switches load balance flowlets
S1
S2
S3
S4
ToR 10
Dest | Best hop | Path util
ToR 10 | S4 | 50%
ToR 1 | S2 | 10%
… | … | 
Dest | Timestamp | Next hop
ToR 10 | 1 | S4
 | … | …
 | … | …
ToR 1
Flowlet table
Best hop table
Data
Notes: The switches then route data packets in the opposite direction by spitting flows into smaller groups of packets called flowlets. Flowlets basically are subsequences of packets in a flow separated by a large enough inter-packet gap so that when different flowlets are sent on different paths, the destination does not see packet reordering with high probability.

## Slide 24: Switches load balance flowlets
S1
S2
S3
S4
ToR 10
Dest | Best hop | Path util
ToR 10 | S4 | 50%
ToR 1 | S2 | 10%
… | … | 
ToR 1
Flowlet table
Best hop table
Data
P4 primitives
RW access to stateful memory
Comparison/arithmetic operators
Dest | Timestamp | Next hop
ToR 10 | 1 | S4
 | … | …
 | … | …
Notes: The switches then route data packets in the opposite direction by spitting flows into smaller groups of packets called flowlets. Flowlets basically are subsequences of packets in a flow separated by a large enough inter-packet gap so that when different flowlets are sent on different paths, the destination does not see packet reordering with high probability.

## Slide 25: Switches load balance flowlets
S1
S2
S3
S4
ToR 10
Dest | Best hop | Path util
ToR 10 | S4 | 50%
ToR 1 | S2 | 10%
… | … | 
ToR 1
Flowlet table
Best hop table
Data
P4 code snippet
if(curr_time - flowlet_time[flow_hash] > THRESH) {
flowlet_hop[flow_hash] =best_hop[packet.dst_tor];
}
metadata.nxt_hop = flowlet_hop[flow_hash];
flowlet_time[flow_hash] = curr_time;
Dest | Timestamp | Next hop
ToR 10 | 1 | S4
 | … | …
 | … | …
Notes: The switches then route data packets in the opposite direction by spitting flows into smaller groups of packets called flowlets. Flowlets basically are subsequences of packets in a flow separated by a large enough inter-packet gap so that when different flowlets are sent on different paths, the destination does not see packet reordering with high probability.

## Slide 26: Evaluated Topology
L1
A1
A2
L2
S1
S2
A4
L4
A3
L3
8 servers
per leaf
40Gbps
40Gbps
10Gbps
Link Failure

## Slide 27: Evaluation Setup
NS2 packet-level simulator
RPC-based workload generator
  Empirical flow size distributions
  Websearch and Datamining
End-to-end metric
  Average Flow Completion Time (FCT)

## Slide 28: Compared with
ECMP
  Flow level hashing at each switch
CONGA’
  CONGA within each leaf-spine pod
  ECMP on flowlets for traffic across pods1
1. Based on communication with the authors

## Slide 29: HULA handles high load much better

## Slide 30: HULA keeps queue occupancy low

## Slide 31: HULA is stable on link failure

## Slide 32: HULA - Summary
  Scalable to large topologies
    HULA distributes congestion state
  Adaptive to network congestion
  Proactive path probing
  Reliable when failures occur
  Programmable in P4!
Notes: This leads to a design that is topology oblivious (it makes no assumptions about symmetry or number of hops in the network)
The distribution of only the relevant utilization state to network switches mitigates concentration of a huge amount of state at the sender.
Since each switch makes the routing decision based on the INT info, there is no separate source routing mechanism necessary.
And most interesting thing is that all this logic is programmable in P4. I can discuss the details offline if you are interested.

## Slide 33: Backup
Notes: Ok, let’s see why correctness is tricky compared to say traditional IP rule caching.

## Slide 34: HULA: Scalable, Adaptable, Programmable
LB Scheme | Congestion aware | Application agnostic | Dataplane timescale | Scalable | Programmable dataplanes
ECMP |  |  |  |  | 
SWAN, B4 |  |  |  |  | 
MPTCP |  |  |  |  | 
CONGA |  |  |  |  | 
HULA |  |  |  |  |