## Slide 1: ProActive Routing In Scalable Data Centers with PARIS
Joint work with Dushyant Arora+ and Jennifer Rexford*
+Arista Networks
*Princeton University
Theophilus Benson
Duke University

## Slide 2: Data Center Networks Must …
Support diverse application
  High throughput/low latency
  Utilize multiple paths
Scale to cloud size
  5-10 million VMs
Support flexible resource utilization
  Support seamless VM mobility

## Slide 3: Evolution of Data Center Networks…
Scalable
Seamless
mobility
Multipath
routing
Layer 2:
Flat Addresses
Layer 3:
Hierarchical Addresses
Overlays:
VL2/Portland
PARIS

## Slide 4: PARIS in a Nutshell…
PARIS is a scalable and flexible flat layer 3 network fabric.
PARIS hierarchically partitions addresses at the core
PARIS runs on a data center of commodity switches

## Slide 5: Outline
Evolution of Data Center Networks
PARIS Architecture
Evaluation and Conclusion

## Slide 6: Evolution of Data Center Networks
Flat layer 2: Spanning Tree
  Uses flooding to discover location of hosts
    Supports seamless VM migration
  Traffic restricted to single network path
Not scalable
Seamless mobility
No Multipath

## Slide 7: Evolution of Data Center Networks
Layer 3:Hierarchical Addresses
  Host locations are predefined
  During VM mobility, IP-addresses change
  Load balances over k shortest paths
Scalable
No seamless mobility
Multipath

## Slide 8: Evolution of Data Center Networks
Overlay solutions: Portland/VL2
  Uses two addressing schemes:
    hierarchical addresses: for routing traffic
    flat addresses: for identifying VMs
Seamless mobility
Multipath
Not scalable

## Slide 9: Overheads introduced by Overlays Solutions…
  Address resolution infrastructure
    Inflated flow startups times
  Switch CPU for encapsulation
  Switch storage for caching address resolutions
Flat-Address
Hierarchical-Address
FA
Payload
HA
Payload
HA
HA
Resolve

## Slide 10: Evolution of Data Center Networks…
Scalable
Seamless
mobility
Multipath
routing
Layer 2:
Flat Addresses
Layer 3:
Hierarchical Addresses
Overlays:
VL2/Portland

## Slide 11: Challenges..
Develop data center network that supports benefits of overlay routing while eliminating ..
  Overheads of caching and packet-encapsulation
  Overheads of address translation

## Slide 12: ProActive Routing In Scalable PARIS Architecture

## Slide 13: Architectural Principles
Flat layer-three network
  Allows for seamless VM mobility
Proactive installation of forwarding state
  Eliminates startup latency overheads
Hierarchical partitioning of network state
  Promotes scalability

## Slide 14: Paris Architecture
Network Controller
End-Hosts:
/32 addresses
Default GW: edge switch
Switches:
Support ECMP
Programmable devices
Network Controller:
Monitors network traffic
Performs traffic engineering
Tracks network topology
Pro-actively installs forwarding entries
Overheads eliminated
Pro-active rule installation  No start-up delay for switch rule installation
No addresses indirection  No address resolution, encapsulation, caching
/32 network addresses  No broadcast traffic; no ARP

## Slide 15: Evolution of Data Center Networks…
Scalable
Seamless
mobility
Multipath
routing
Layer 2:
Flat Addresses
Layer 3:
Hierarchical Addresses
Overlays:
VL2/Portland
PARIS

## Slide 16: Paris Network Controller
Switches have 1 million entries
  But data center has 5-10 million VMs
  Each pod has ~100K VMs
Network Controller
Pod-Addressing
Core-Addressing
Pod switch track addresses for all VMs in the pod
Partition IP-Address across core devices

## Slide 17: Pod-Addressing Module
Edge & aggregation addressing scheme
  Edge: stores address for all connected end-hosts
  Pod: stores addresses for all end-hosts in pod
10.10.10.1
10.10.10.2
10.10.10.3
10.10.10.4

## Slide 18: Pod-Addressing Module
Edge & aggregation addressing scheme
  Edge: stores address for all connected end-hosts
  Agg: stores addresses for all end-hosts in pod
10.10.10.1
10.10.10.2
10.10.10.3
10.10.10.4
10.10.10.1->2
10.10.10.2->2
10.10.10.3->1
10.10.10.4->1
10.10.10.1->1
10.10.10.2->1
10.10.10.3->2
10.10.10.4->2
10.10.10.1->1
10.10.10.2->1
10.10.10.3->1
10.10.10.4->1
default->(2,3)
default->(2,3)
1
2
3

## Slide 19: Core Addressing-Modules
Partitions the IP-space into virtual-prefix
  Each core is an Appointed prefix switch (APS)
  Tracks all address in a virtual-prefix
10.0.0.0/14

## Slide 20: Core Addressing-Modules
Partitions the IP-space into virtual-prefix
  Each core is an Appointed prefix switch (APS)
  Tracks all address in a virtual-prefix
10.0.0.0/15
10.3.0.0/16
10.0.0.0/16
10.1.0.0/16
10.2.0.0/16

## Slide 21: Core Addressing-Modules
Partitions the IP-space into virtual-prefix
  Each core is an Appointed prefix switch (APS)
  Tracks all address in a virtual-prefix
10.0.0.0/15
10.3.0.0/16
10.0.0.0/16
10.1.0.0/16
10.2.0.0/16

## Slide 22
1
2
3
4
1
2
1
2
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.0.0.0/16->{1,2}
DIP:10.1.0.0/16->{3,4}
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:10.1.0.0/16->3
DIP:10.0.0.3->2
DIP:10.0.0.4->2
DIP:10.2.0.0/16->4
DIP:10.3.0.0/16->4
DIP:10.0.0.0/16->3
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:10.2.0.0/16->3
DIP:10.3.0.3->2
DIP:10.3.0.4->2
DIP:10.0.0.0/16->4
DIP:10.1.0.0/16->4
DIP:10.3.0.0/16->3
DIP:10.3.0.2->1
10.3.0.1
10.0.0.1

## Slide 23
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:10.2.0.0/16->3
DIP:10.3.0.3->2
DIP:10.3.0.4->2
DIP:10.0.0.0/16->4
DIP:10.3.0.0/16->{1,2}
DIP:10.1.0.0/16->4
DIP:10.2.0.0/16->{3,4}
1
2
3
4
1
2
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:10.1.0.0/16->3
DIP:10.0.0.3->2
DIP:10.0.0.4->2
DIP:10.2.0.0/16->4
DIP:10.0.0.0/16->{1,2}
DIP:10.3.0.0/16->4
DIP:10.1.0.0/16->{3,4}
DIP:10.0.0.0/16->3
DIP:10.3.0.0/16->3
DIP:10.3.0.2->1
Limitations
No Load balancing between the core nodes
Multi-path in core is not utilized!

## Slide 24
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:10.2.0.0/16->3
DIP:10.3.0.3->2
DIP:10.3.0.4->2
DIP:10.0.0.0/16->4
DIP:10.3.0.0/16->{1,2}
DIP:10.1.0.0/16->4
DIP:10.2.0.0/16->{3,4}
1
2
3
4
1
2
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:10.1.0.0/16->3
DIP:10.0.0.3->2
DIP:10.0.0.4->2
DIP:10.2.0.0/16->4
DIP:10.0.0.0/16->{1,2}
DIP:10.3.0.0/16->4
DIP:10.1.0.0/16->{3,4}
DIP:10.0.0.0/16->3
DIP:10.3.0.0/16->3
DIP:10.3.0.2->1
Limitations
No Load balancing between the core nodes
Multi-path in core is not utilized!
Not utilized
Highly utilized

## Slide 25
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:10.2.0.0/16->3
DIP:10.3.0.3->2
DIP:10.3.0.4->2
DIP:10.0.0.0/16->4
DIP:10.3.0.0/16->{1,2}
DIP:10.1.0.0/16->4
DIP:10.2.0.0/16->{3,4}
1
2
3
4
1
2
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:10.1.0.0/16->3
DIP:10.0.0.3->2
DIP:10.0.0.4->2
DIP:10.2.0.0/16->4
DIP:10.0.0.0/16->{1,2}
DIP:10.3.0.0/16->4
DIP:10.1.0.0/16->{3,4}
DIP:10.0.0.0/16->3
DIP:10.3.0.0/16->3
DIP:10.3.0.2->1
DIP:10.0.0.0/14->{3,4}
DIP:10.0.0.0/14->{3,4}
High-BW PARIS:
Connect core nodes in a mesh
Change rules at aggregation to load balance across core nodes
Use Valiant Load-balancing in the core

## Slide 26
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:10.2.0.0/16->3
DIP:10.3.0.3->2
DIP:10.3.0.4->2
DIP:10.0.0.0/16->4
DIP:10.3.0.0/16->{1,2}
DIP:10.1.0.0/16->4
DIP:10.2.0.0/16->{3,4}
1
2
3
4
1
2
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:10.1.0.0/16->3
DIP:10.0.0.3->2
DIP:10.0.0.4->2
DIP:10.2.0.0/16->4
DIP:10.0.0.0/16->{1,2}
DIP:10.3.0.0/16->4
DIP:10.1.0.0/16->{3,4}
DIP:10.0.0.0/16->3
DIP:10.3.0.0/16->3
DIP:10.3.0.2->1
DIP:10.0.0.0/14->{3,4}
DIP:10.0.0.0/14->{3,4}
High-BW PARIS:
Connect core nodes in a mesh
Change rules at aggregation to load balance across core nodes
Use Valiant Load-balancing in the core

## Slide 27
DIP:10.3.0.1->1
DIP:10.3.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.3.0.2->1
DIP:10.2.0.0/16->3
DIP:10.3.0.3->2
DIP:10.3.0.4->2
DIP:10.0.0.0/16->4
DIP:10.3.0.0/16->{1,2}
DIP:10.1.0.0/16->4
DIP:10.2.0.0/16->{3,4}
1
2
3
4
1
2
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:*.*.*.*->{2,3}
DIP:10.0.0.1->1
DIP:10.0.0.2->1
DIP:10.1.0.0/16->3
DIP:10.0.0.3->2
DIP:10.0.0.4->2
DIP:10.2.0.0/16->4
DIP:10.0.0.0/16->{1,2}
DIP:10.3.0.0/16->4
DIP:10.1.0.0/16->{3,4}
DIP:10.0.0.0/16->3
DIP:10.3.0.0/16->3
DIP:10.3.0.2->1
DIP:10.3.0.1->{7,8}
DIP:10.3.0.1->1
DIP:10.3.0.1->1

## Slide 28: Evaluation

## Slide 29: Evaluation
How does PARIS scale to large data centers?
Does PARIS ensure good performance?
How does PARIS perform under failures?
How quickly does PARIS react to VM migration?

## Slide 30: Evaluation
How does PARIS scale to large data centers?
Does PARIS ensure good performance?
How does PARIS perform under failures?
How quickly does PARIS react to VM migration?

## Slide 31: TestBed
  Emulate data center topology using Mininet
    Generate traffic using IPerf
    Random traffic traffic matrix
  Implemented PARIS on NOX
  Data center topology
    32 hosts, 16 edge, 8 aggregation, and 4 core
    No over-subscription
  Link capacity:
    Server Uplinks: 1Mbps
    Switch-Switch: 10Mbps

## Slide 32: Scaling to Large Data Centers
NoviFlow has developed switches with 1 million entries [1].
Chart: Flow table size
| 4000.0 | 16000.0 | 32000.0 | 64000.0
 | 65536 | 262144 | 524288 | 1048576
128 ports*
[1] NoviFlow. 1248 Datasheet. http://bit.ly/1baQd0A.

## Slide 33: Does PARIS Ensure Good Performance?
How low is latency?
  Recall: random traffic matrix.
Communication Pattern | Latency
Inter-pod | 61us
Intra-pod | 106us

## Slide 34: Summary
PARIS achieves scalability and flexibility
  Flat layer 3 network
  Pre-positioning forwarding state in switches
  Using topological knowledge to partition forwarding state
Our evaluations show that PARIS is practical!
  Scales to large data-centers
  Can be implemented using existing commodity devices

## Slide 35: Questions