## Slide 1: SPINE: Surveillance protection in the network Elements
Trisha Datta, Nick Feamster, Jennifer Rexford, Liang Wang
Princeton University

## Slide 2: Privacy Threat from Plaintext IP Addresses
IP addresses can reveal sensitive information about senders/recipients
Threat of surveillance by intermediate networks
Real world example: Brazil, Portugal, USA (adversary)
Threat model:
Trusted
Entity #2
Trusted
Entity #1
Untrusted
Entity
R1
R2
Notes: Elaborate on what IP addresses reveal (website, who user is, geographic location, etc.)

## Slide 3: Deployment Challenges in Existing Solutions
IPSec Tunnels: encrypt entire packet
  Computationally expensive
Network-Layer Anonymity Systems: nodes on path implement privacy-preserving protocol (e.g., Tor)
  Require participation from (potentially adversarial) intermediate nodes
  Require participation from (probably uninformed) end-users
We want a faster solution with fewer participants!

## Slide 4: Recent Technologies and Trends
TLS use is widespread  payloads are encrypted
Programmable switches let us manipulate packets at switch hardware rates
Increasing ubiquity of IPv6 (with longer 128-bit IP addresses) in network core

## Slide 5: SPINE Contributions
SPINE: practical solution to prevent an adversary along an end-to-end path from observing source and destination IP addresses.
  Processing performed at switch hardware rates
  No cooperation from intermediate autonomous systems
  No involvement from end users
  Flow-packet “unlinkability”

## Slide 6: Encrypting Relevant Header Fields
How do we prevent information leakage from IP addresses and TCP sequence/acknowledgment numbers?
  Encryption!
Trusted
Entity #2
Trusted
Entity #1
Untrusted
Entity
R1
Original Traffic
SPINE (encrypted) Traffic
R2
Central Controller
SPINE Tables and Keys
SPINE
SPINE
Notes: - See where everything happens; show where keys are being installed from above (central controller)

## Slide 7: Efficient Cryptography on Header Fields
One-time pad encryption – requires only one XOR operation
Encrypt(ip, k) = ip ⊕ H(k, nonce)
  ip: IP address (or TCP seq/ack no.)
  k: secret key
  nonce: public randomly-generated bit string
  H: keyed hash function
Different nonce for each packet  flow-packet unlinkability
Encrypted IPv4 Address
Hash Function
Nonce
One-Time Pad
Original IPv4 Address

## Slide 8: Rotating Encryption Keys
We want:
  No repeated one-time pads
  To thwart authorities who might demand packet decryption
Solution: rotate keys
To prevent inconsistency, we use version numbers and remember old keys for t seconds

## Slide 9: Challenges with Encrypting IP Addresses
Sending encryption metadata with packet
Discerning which traffic is SPINE traffic
Ensuring successful routing
Solution: we need more space in the header  IPv6

## Slide 10: SPINE Example
Encrypt and replace IPv4 header with IPv6 header
Trusted
Entity #2
Trusted
Entity #1
Untrusted
Entity
R1
Original Traffic
SPINE (encrypted) Traffic
R2
Decrypt and restore original IPv4 header
Host A
Host B
SPINE
SPINE

## Slide 11: IPv4 to IPv6 Header Transformation
Encrypted IPv4 Address
Reserved IPv6 Prefix
New IPv6 Address
Version #
Nonce
Most fields transferred directly
New IPv6 address
  Encrypted IPv4 address
  Encryption metadata
  “Reserved IPv6 prefix” – owned and announced by receiving trusted entity but no services offered there

## Slide 12: P4 Implementation
Advent of high-speed programmable data planes  packet manipulation
P4 programs meant to run at line rates – “If it fits, it runs”
  Limit on operations (e.g., one-time pad encryption)
P4 programs: series of match-action tables

## Slide 13: P4 Pipeline
Trusted
Entity #1
Untrusted
Entity
R1
R2
Trusted
Entity #2
Check IPv6 Dst Addr  Decrypt if necessary
Set forwarding port
Check IPv4 Dst Addr  Encrypt if necessary
Parse headers
Deparse headers
SPINE Tables
Central Controller
SPINE Program
Routing Tables
SPINE
SPINE

## Slide 14: P4 Prototype and Resource Requirements
Nonce generation: P4 random() function
Hash function: SipHash
  Pseudorandom function
  Fast on short inputs
Central controller that controls keys and versions
Resource Requirements: ~140 KB
Ran simulations on Mininet software simulator
Working on running SPINE on Barefoot Tofino switches
Notes: Quantify overhead from adding IPv6 header
  20 bytes in IPv4 header
  40 bytes in IPv6 header
  20 bytes of overhead in header
Jumbo frames in core of internet

## Slide 15: Conclusion
Header fields can leak information to intermediate networks
Developed SPINE to combat this threat
  No cooperation from intermediate autonomous systems
  No involvement from end users
  Uses efficient encryption and implementable in P4
Using IPv6 bits for encryption purposes
Github repo: https://github.com/SPINE-P4/spine-code
Thank you for your time!
Notes: How often do you cycle keys? use packets/second in core to calculate

## Slide 16: Why do we need SipHash?
SipHash is a pseudorandom function
  PRF f and key k
  Given x, f(k, x), and y, an attacker cannot guess f(k, y)
One-time pad encryption: E(ip) = ip ⊕ p, where p = f(k, nonce)
  ip ⊕ E(ip) = p
  Attacker can send packet with IP address ip, observe E(ip), and recover p
  If f is not a PRF, then p can leak information about k