## Slide 1: Campus network as a P4 Lab
Xiaoqi Chen, Princeton University
https://p4campus.cs.princeton.edu

## Slide 2: Why deploy in campus?
A tangible first step before carrier / data center networks
Iterate faster “local” collaboration / approval
Benefits the community students enjoy faster network

## Slide 3: Campus network as a testbed!
A representative enterprise network
  Internet peering, many routers, firewall, different user roles
Same problems as all networks
  Congestion, drops, failures, attacks
An open and dynamic network
  BYOD, a lot of experimental stuff, less restrictive access

## Slide 4: P4 Apps for campus network
Security
  OS fingerprint analysis
  Intrusion detection offload
  Honeypot / Deception
Performance
  Heavy hitter detection
  Queue and microburst analysis
  RTT statistics
  DNS cache
Privacy
  Trace anonymization
  Surveillance protection

## Slide 5: P4 Apps for campus network
Security
  OS fingerprint analysis
  Intrusion detection offload
  Honeypot / Deception
Performance
  Heavy hitter detection
  Queue and microburst analysis
  RTT statistics
  DNS cache
Privacy
  Trace anonymization
  Surveillance protection
Green: already deployed
Yellow: developing P4 program

## Slide 6: Our workflow
Establish collaboration with campus network operator
  Find collaborator, point of contact
  Identify potential use cases of P4
Administrative approval
  data management scheme & anonymization
Develop and deploy individual P4 ”apps”

## Slide 7: Lifecycle of each “P4 app”
Concept
Develop ideas
BMV2 prototype
Trace test
Simulation
Tofino prototype
Paper writing
Deploy & Iterate
Trace test
Debug with live traffic
Write non-P4 components

## Slide 8
OIT router
P4 switch
Peering with
Internet2
OIT core switch
P4 switch
Forrestal campus supercomputing center
CS Dept gateway
P4 switch
P4 switch
CS Dept cluster
OIT core switch
P4 switch
Peering with local ISPs
Internet
CS Dept gateway
CS colo
Other clusters
Peering with
ESNet
ESNet
I2

## Slide 9: Case study 1: PRECISION
Goal: Monitor heavy hitter flows in the network.
Challenge:
  Border link speed is 10/100Gbps, can’t capture & analyze on CPU
  Sampling captures the largest flows, but miss medium-sized flows
Use a heavy-hitter detection P4 program
  Maintain & update a list of heavy flows in data plane
See our ICNP’18 paper for more detail Efficient Measurement on Programmable Switches Using Probabilistic Recirculation. Ran Ben-Basat, Xiaoqi Chen, Gil Einziger, Ori Rottenstreich

## Slide 10: Findings
10Gbps mirrored traffic from border router
Top-1 host is an open source mirror site
mirror.math.princeton.edu

## Slide 11: Case study 2: Snappy
Issue: a link with high packet drop and low average link utilization
  Microburst?
  Which flows caused the drop?
Challenge:
  Bursts happen at short timescale
  Legacy routers do not support reporting queuing statistics
Use an off-path queuing analytics P4 program
See our CoNEXT’19 paper for more detail Fine-Grained Queue Measurement in the Data Plane. Xiaoqi Chen, Shir Landau Feibish, Yaron Koral, Jennifer Rexford, Ori Rottenstreich, Steven A Monetti, Tzuu-Yi Wang
Border router
Target router
Internet2
100G
100G
10G, lossy
10G
10G
10G
P4 Programmable switch

## Slide 12: Findings
For each high loss event, there are bursts of packets from PerfSonar servers from Internet2
  Maybe: simultaneous throughput tests?
  Claim: they’ll be scheduled “exclusively”?
For other high queue utilization events without loss, there are only one throughput testing flow

## Slide 13: Findings
Congestion Control failing
Congestion control working well
Very few packet drops
Only one incoming throughput test
Simultaneous tests

## Slide 14: Lesson learned
From BMV2+Mininet to Tofino+Campus Net
  Fitting and adapting P4
    Think about hardware while designing algorithm
  Debugging back and forth unavoidable, need fast iteration
Can provide value for campus network
  Even small improvement / innovation can be useful for operators!

## Slide 15: Share our apps, share our methodology
Contact us for code sharing
  Build a collection of apps!
Work with campus network operators everywhere!
  Deploy P4 into many academic networks
  Start administrative approval process early
Reach out to us: p4campus@princeton.edu
Learn more: https://p4campus.cs.princeton.edu
Notes: If you have a switch, you can also run our code (via Barefoot’s FASTER program). Reach out to us if you need any help