## Slide 1: AES in P4 using scrambled lookup tables
Xiaoqi Chen

## Slide 2: Secure Apps Need Secure Crypto
“Never roll your own crypto”!
  CRC-32 is likely not secure enough…
Data plane: many computational constraints
  Short pipeline, simple arithmetic
Is standardized crypto still possible?
  Maybe?

## Slide 3: AES: An Intro
NIST standard encryption algorithm
“Block cipher”, encrypt data 16 bytes at a time
Uses 10, 12, or 14 encryption rounds
Each round:
  AddRoundKey
  SubBytes
  ShiftRows
  MixColumns
NSA Approved

## Slide 4: An AES Round
a0,0 | a1,0 | a2,0 | a3,0
a0,1 | a1,1 | a2,1 | a3,1
a0,2 | a1,2 | a2,2 | a3,2
a0,3 | a1,3 | a2,3 | a3,3
b0,0 | b1,0 | b2,0 | b3,0
b0,1 | 01 | b2,1 | b3,1
b0,2 | b1,2 | b2,2 | b3,2
b0,3 | b1,3 | b2,3 | 04
c0,0 | c1,0 | c2,0 | c3,0
c0,1 | 7B | c2,1 | c3,1
c0,2 | c1,2 | c2,2 | c3,2
c0,3 | c1,3 | c2,3 | F2
k0,0 | k1,0 | k2,0 | k3,0
k0,1 | k1,1 | k2,1 | k3,1
k0,2 | k1,2 | k2,2 | k3,2
k0,3 | k1,3 | k2,3 | k3,3
16-byte round key
In | 00 | 01 | 02 | 03 | 04 | 05 | …
Out | 63 | 7B | 77 | 7B | F2 | 6B | …
Substitution box (S-box)
AddRoundKey:
using XOR
(2) SubBytes: lookup in S-box

## Slide 5: An AES Round
c0,0 | c1,0 | c2,0 | c3,0
c0,1 | c1,1 | c2,1 | c3,1
c0,2 | c1,2 | c2,2 | c3,2
c0,3 | c1,3 | c2,3 | c3,3

## Slide 6: An AES Round
c0,0 | c1,0 | c2,0 | c3,0
c0,1 | c1,1 | c2,1 | c3,1
c0,2 | c1,2 | c2,2 | c3,2
c0,3 | c1,3 | c2,3 | c3,3
c0,0 | c1,0 | c2,0 | c3,0
c1,1 | c2,1 | c3,1 | c0,1
c2,2 | c3,2 | c0,2 | c1,2
c3,3 | c0,3 | c1,3 | c2,3
d0,0 | d1,0 | d2,0 | d3,0
d0,1 | d1,1 | d2,1 | d3,1
d0,2 | d1,2 | d2,2 | d3,2
d0,3 | d1,3 | d2,3 | d3,3
(3) ShiftRows: each row cyclically shifted by 0, 1, 2, or 3 positions
(4) MixColumns: Polynomial Multiplication under GF(28), modulus (x4+1)
a(x) = | 3x3+x2+x+2
b(x) = | c1,0x3+c2,1x2+c3,2x+c0,3
d(x) = | a(x)⊗b(x) mod (x4+1)
= | d1,0x3+d1,1x2+d1,2x+d1,3

## Slide 7: An AES Round
d0,0 | d1,0 | d2,0 | d3,0
d0,1 | d1,1 | d2,1 | d3,1
d0,2 | d1,2 | d2,2 | d3,2
d0,3 | d1,3 | d2,3 | d3,3
a0,0 | a1,0 | a2,0 | a3,0
a0,1 | a1,1 | a2,1 | a3,1
a0,2 | a1,2 | a2,2 | a3,2
a0,3 | a1,3 | a2,3 | a3,3
Rinse and repeat!
AES-128: 10 rounds
AES-192: 12 rounds
AES-256: 14 rounds

## Slide 8: Different Optimization Objectives
Embedded system
Very small memory
  Don’t use large lookup tables
Sequential computation
Run many cycles
P4 switch
Relatively larger memory
  For routing tables
Parallel data flow
Challenge: limited # stages

## Slide 9: Solution: Scrambled Lookup Table
a0,0 | a1,0 | a2,0 | a3,0
a0,1 | a1,1 | a2,1 | a3,1
75 | a1,2 | a2,2 | a3,2
a0,3 | a1,3 | a2,3 | a3,3
c0,0 | c1,0 | c2,0 | c3,0
c0,1 | c1,1 | c2,1 | c3,1
F2 | c1,2 | c2,2 | c3,2
c0,3 | c1,3 | c2,3 | c3,3
12 | k1,0 | k2,0 | k3,0
34 | k1,1 | k2,1 | k3,1
71 | k1,2 | k2,2 | k3,2
55 | k1,3 | k2,3 | k3,3
16 tables per round,
one for each ki,j
Pre-computed Scrambled Lookup Tables
In | 00 | 01 | 02 | 03 | 04 | 05 | …
In XOR k0,0 | 12 | 13 | 10 | 11 | 16 | 17 | …
Out | 63 | 7B | 77 | 7B | F2 | 6B | …
In | 00 | 01 | 02 | 03 | 04 | 05 | …
In XOR k1,0 | 34 | 35 | 36 | 37 | 30 | 31 | …
Out | 63 | 7B | 77 | 7B | F2 | 6B | …
In | 00 | 01 | 02 | 03 | 04 | 05 | …
In XOR k0,2 | 71 | 70 | 73 | 72 | 75 | 74 | …
Out | 63 | 7B | 77 | 7B | F2 | 6B | …
…

## Slide 10: Solution: Scrambled Lookup Table
Use 160x~224x memory space to save XORs
  Input block -> Lookup -> XOR -> Output block
  Theoretical minimum: 2 stage per round
Each table costs 1KB
Justifiable in switches: short pipeline, MBs of memory

## Slide 11: Evaluation
Does it actually fit?
  Theoretically SLTs costs 160~224 KB of memory in total
  In practice, occupied <15% of SRAM on Tofino v1
  Other resource utilization are negligible
So, what is the real-world performance?
  10Gbit/s @ two rounds per pass (200Gbps recirculation limit)
  122% improvement compared with baseline (one round per pass)

## Slide 12: Evaluation

## Slide 13: Evaluation
=1.3x =0.3x
Tofino Wedge100-32x, $8000
MacBook Air 13” 2017, $1200 Intel i7 (AES-NI), 2.2Ghz 2 cores
MacBook Pro 16” 2019, $2400 Intel i7 (AES-NI), 2.6Ghz 6 cores
Use 50% ports for recirculation
=11x =2.4x

## Slide 14: Conclusion & Future Directions
AES runs on P4 switches!
  Please, avoid hand-rolled crypto
  Scrambled Lookup Table: save XORs using 160~224KB memory
  Two rounds per pass, improves throughput by 122%
Tofino v1 is not the best device to run AES
  Other algorithms? Is Feistel Cipher more PISA-friendly?
  Fewer rounds?
  Dedicated crypto co-processor in switches?
Our P4 code is open-source! github.com/Princeton-Cabernet/p4-projects