## Slide 1: Measuring TCP RTT in the data plane
Xiaoqi Chen, Hyojoon Kim, Javed M Aman,
Willie Chang, Mack Lee, Jennifer Rexford

## Slide 2: Why measure round-trip time?
Security
  BGP hijack, inter-ISP path change
  IP spoofing
Performance
  Persistent link congestion
  Infer user Quality of Experience (QoE)

## Slide 3: Monitoring at a vantage point
Internet
Client
External Leg
Internal Leg
Vantage Point
Passive monitoring: split client-server RTT into two legs1
Run a programmable switch at the vantage point?
  Line-rate traffic, multiple samples per flow
  Directly in data plane, enabling real-time reroutes
1Cziva et al. Ruru: High-speed, Flow-level Latency Measurement and Visualization of Live Internet Traffic. SIGCOMM 2017

## Slide 4: TCP sequence numbers
Internet
Client
External Leg
Internal Leg
Vantage Point
SYN
SYN/ACK
ACK
SEQ
ACK
ACK
SEQ
External Leg RTT
Internal Leg RTT
External Leg RTT
Internal Leg RTT

## Slide 5: A table with timestamps
Flow id, eACK | Timestamp
(A->B, 1001) | T=101
(A->B, 1004) | T=105
(A->C, 1050) | T=122
(D->E, 1020) | T=107
Outgoing Packet A->B, SEQ=1001, Len=3 (eACK=1004)
Incoming Packet C->A, ACK=1050
Insert record
Match & erase
T=105
T=125
expected ACK:
SEQ + Len
RTT = 3

## Slide 6: Challenge: delayed ACK
Issue 1: ACK is not immediate, might be delayed for 50ms
Solution: heuristics
  Look at ACKs for MTU-sized packets, likely not experiencing delay
Issue 2: Many packets never receive their ACK
Solution: lazy-expiration of entries
  An entry is considered timed out when timestamp is too old
  Upon table insertion, check timestamp and erase old entry

## Slide 7: Multi-stage hash tables
Per-stage random hash functions
Multiple chances to sidestep hash collisions
Stage 1 |  | Stage 2 |  | Stage 3 |  | Stage 4
Occupied |  | Occupied |  |  |  | 
Expired |  |  |  | Expired |  | Occupied
Occupied |  | Occupied |  |  |  | 
Occupied |  | Expired |  | Occupied |  | 
 |  | Occupied |  | Occupied |  | Expired
Occupied |  |  |  |  |  | 
Outgoing Packet
Insert record
h2(fid, eACK)
h3(fid, eACK)
h4(fid, eACK)
h1(fid, eACK)
Flow id: *
eACK: ***
T=*
Inserted

## Slide 8: Multi-stage hash tables
Check every stage, until a match is found
Stage 1 |  | Stage 2 |  | Stage 3 |  | Stage 4
Occupied |  | Occupied |  |  |  | 
Expired |  |  |  | Expired |  | Occupied
Expired |  | Occupied |  |  |  | 
Expired |  | Expired |  | Expired |  | 
 |  | Occupied |  | Occupied |  | 
Occupied |  |  |  |  |  | 
Incoming Packet
Query record
h2(fid, ACK)
h3(fid, ACK)
h4(fid, ACK)
h1(fid, ACK)
T=*
Matched RTT
Occupied
fid reversed
ACK: ***

## Slide 9: Evaluation
Traffic: captured from 10Gbps campus border links
Metric: % of RTT samples matched
Parameters for multi-stage hash table:
  Size per table (# of entries)
  Total number of tables

## Slide 10: Evaluation
100%
50%
0%
212
214
216
Size per table (# entries)
215
213
75%
25%
Match rate
Better
(32KB)
(0.5MB)

## Slide 11: Deployment
University campus deployment
  Mirrored traffic, non-invasive
  External leg: cloud service latency monitoring
  Internal leg: Wi-Fi client latency diagnostics
Internet
External Leg
Internal Leg
Vantage Point
Campus
Mirrored
Tofino

## Slide 12: Summary, Q&A
Match TCP SEQ/ACK numbers for RTT samples
Multi-stage hash table with lazy expiration of entries
Tested & deployed on 10Gbps campus border links
Our P4 code is open-source! github.com/Princeton-Cabernet/p4-projects